Consumer Electronic Control (CEC)
- An optional supplement to HDMI
- Provides high-level control functions between all of the various audiovisual products in a user's environment.
- An extension of AV.link EN 50157-2-[123] (scart)
- Implemented in HDMI receivers/transmitters and USB HDMI-passthrough devices.
- Status of CEC support in DisplayPort is unclear: technically possible, but no standard seems to exist for it.

---
In Short
- One-wire “party-line” which connects up to 10 audiovisual (AV) devices
- Very small data packets, 16 Bytes
- Very low data rate ~400 bits/s
- Pin 13 on the HDMI connector (type A)

---
CEC message format
Header Byte + 0 to 15 Data Bytes
Start Bit	Header Byte
	3	2	1	0	3	2	1	0	-	-
	Initiator				Destination				EOM	ACK
Initiator: 4 bits: initiator logical address
Destination: 4 bits: destination logical address
EOM: 1 bit, end of message, last byte of frame
ACK: 1 bit, acknowledge of direct addressed frames, reject for broadcast
First Data Byte is operation code (opcode, command)
A single Header Byte with no Data Bytes is a “poll” message
Data Bytes
8 data bits (operation code)	EOM	ACK

---
Addressing
Each device is assigned two addresses
- Physical address: Hierarchy placement
  Range: 0.0.0.0 – F.F.F.F
  root device: 0.0.0.0, HDMI Sink, typically a TV
  First device: 1.0.0.0 Device connected to HDMI port 1 on root device
  Second device: 2.0.0.0 Device connected to HDMI port 2 on root device
  Third device: 1.1.0.0 Device connected to HDMI port 1 on first device
  Sources get their Physical address from the EDID obtained from the sink
- Logical address: Product type dependent
  Range: 0 - 15
  0: TV (root device) 8: Playback device 2
  1: Recording device 1 9: Recording device 3
  2: Recording device 2 10: Tuner 4
  3: Tuner 1 11: Playback device 3
  4: Playback device 1 12: Reserved
  5: Audio system 13: Reserved
  6: Tuner 2 14: Specific use
  7: Tuner 3 15: Unregistered (as Initiator address) Broadcast (as Destination address)

---
Topology example

---
End-User Features (1.4a)
- One Touch Play - Allows a device to be played and become the active source with a single button press.
- System Standby - Enables the user to switch all devices to the Standby state with one button press.
- One Touch Record - Offers a What You See Is What You Record (WYSIWYR) facility, meaning that whatever is shown on the TV screen is recorded on a selected Recording Device.
- Timer Programming – Allows the user to program the timers in a Recording Device from an EPG running on a TV or STB.
- Deck Control - Enables a device to control (e.g. play, fast forward etc.) and interrogate a Playback Device (a deck).

---
End-User Features (cont)
- Tuner Control - Allows a device to control the tuner of another device.
- Device Menu Control - Enables a device to control the menu of another device by passing through user interface commands.
- Remote Control Pass Through - Enables remote control commands to be passed through to other devices within the system.
- System Audio Control – Allows an Audio Amplifier / Receiver to be used with the TV. The volume can be controlled using any the remote controls of any suitably-equipped devices in the system.

---
Supporting Features (1.4a)
- Device OSD Name Transfer - Enables devices to upload their preferred OSD name to the TV. The TV can then use this name in any menus associated with that device.
- Device Power Status – Allows the current power status of a device to be discovered.
- OSD Display - Enables a device to use the on-screen display of the TV to display text strings.
- Routing Control - Allows the control of CEC Switches for streaming of a new source device.
- System Information - Queries the system to determine device addresses and language.
- Vendor Specific Commands - Allows a set of vendor-defined commands to be used between devices of that vendor.
- Audio Rate Control – Allows an Amplifier to fractionally increase or decrease the playback rate of an audio source.
  (new features in HDMI 1.4a)
- Audio Return Channel Control – Controls the Audio Return Channel (ARC) part of the HDMI Ethernet and Audio Return Channel (HEAC).
- Capability Discovery and Control – Controls HDMI Ethernet Channel (HEC) part of HEAC.

---
Capability Discovery and Control (CDC) for HEAC
(HDMI Ethernet and Audio Return Channel)
- New in HDMI 1.4a
- HEAC provides a full duplex connection between HDMI devices which conforms to 100Base-TX IEEE 802.3 Standard. This is defined as HDMI Ethernet Channel (HEC)
- HEAC provides audio data streaming which conforms to IEC 60958-1 standard from an HDMI Sink to an HDMI Source or repeater. This is defined as Audio Return Channel (ARC)
- HEAC utilizes the Utility (14) and Hot Plug Detect (19) lines for signal transmission
- HEAC uses CDC for Capability Discovery and Control.

---
CDC Message frame
- The CEC command-set is expanded with “CDC commands”
- CDC and HEC/ARC is dependent on the CEC protocol to function
- A Device might support only CDC commands or the full CEC command-set
	1 Byte	1 Byte	2 Bytes	1 Byte	0 – 11 Bytes
Start Bit	CEC Header	CEC Opcode / 0xF8	Initiator / Physical / Address	CDC / Opcode	CDC / Parameters
CDC Arbitration

---
CDC and HEC (HDMI Ethernet Channel)
- A HEC capable Device sends CDC messages via CEC to detect the presence of other HEC capable devices
- HEC capable devices then reply if they support HEC and the current state
- The following messages are used for the capability discovery and control of the HDMI Ethernet Channel
  <CDC_HEC_Discover>
  <CDC_HEC_InquireState>
  <CDC_HEC_ReportState>
  <CDC_HEC_SetState>
  <CDC_HEC_RequestDeactivation>
  <CDC_HEC_NotifyAlive>
  <CDC_HEC_SetStateAdjacent>

---
CDC and HDP (Hot Plug Detect)
- Devices that support HEC uses the physical HPD pin for the Ethernet data transfer
- HDMI Sinks must maintain the physical HPD pin high to not disturb HEC transmission
- The HPD pin functionality is replaced with CDC messages
  <CDC_HPD_SetState>
  <CDC_HPD_ReportState>

---
CDC and ARC (Audio Return Channel)
The following CEC messages are used between ARC capable HDMI devices to configure and control ARC
<Initiate ARC>
<Report ARC Initiated>
<Report ARC Terminated>
<Request ARC Initiation>
<Request ARC Termination>
<Terminate ARC>

---
Trade Names
- Anynet+ (SAMSUNG)
- BRAVIA Link (Sony)
- Kuro Link (Pioneer)
- EasyLink (Philips)
- SimpLink (LG)
- VIERA link (Panasonic)

---
Summary
- CEC is everything but the kitchen sink.
- The CDC functionality requires that part of the CEC protocol (discovery) is implemented in kernel space: handling ARC and HPD should not be userspace-visible.
- The remote control passthrough could be done in userspace or kernelspace (RC subsystem).
- The remainder is all userspace.

---
Questions
- Should CEC be a separate device (/dev/cecX), or be part of v4l2-subdev/drm devices?
- The advantage of integrating this in V4L2 is that you get all the event handling support for free.
- The disadvantage is that apps will have to use different APIs depending on whether V4L2 or DRM is used.
- Inclined to create separate cec devices. What's the opinion of the drm devs?

---
Implementation Proposal
- Proposal assumes new cecX devices.
- Drivers just needs to implement basic CEC receive/transmit functionality. They register those functions with the CEC core. Some notification mechanism is needed as well (CDC).
- CEC framework to do discovery/CDC. Must use kernel threads or something due to the very slow transmission speeds.
- Userspace API should be event based as well. Ideal if select() can be used to get events, just as V4L2 does.
- A userspace reference library should be created. Add to v4l-utils.git?